## Slide 1
Computer Organization and Assembly Language
Week-03

## Slide 2
Grading Policy:
Assignments: 10%
Quiz: 20%
Mid-term exams: 25% (10 + 15)
CP: 5%
Final exam: 40%
Instructor: Muhammad Usama
Email: m.usama@nu.edu.pk
Office:
Office Hours: Monday and Tuesday (09 am to 11 PM)
Lectures: 2 Lectures/week
Lab: 01 Credit
Logistics Update
Since COAL is a core course for the computer science program, as per NUCES policy the absolute grading willbe observed.
Reading material: (Soft copies of the material will be released before/after the class)
The elements of computing systems by Noam Nisam and Shimon Schocken 2nd Edition.
x86 Assembly language by Kip Irvin (Latest Edition)
Assembly Language Notes by Belal Muhammad Hashmi and Junaid Haroon
System on Chip (SoC) Material from various sources
Updates:
Reading material updated on the Google classroom.
Quiz 2 will be on 2nd lecture of this week.
Material will be from 1st lecture till the end of the first lecture.
Please get nasm, dosbox, AFD sorted by the end of this week as the first set of assignment questions will be released early next week.

## Slide 3
Agenda
Data Declaration
Direct Addressing
Register Indirect Addressing
Register + Offset Addressing
Segment Association
Quiz 2

## Slide 4
Data Declaration
Immediate Operand
Can we write a useful program using immediate operands?
Opcode for Immediate Operands:
mov ax, 5 ===> B80500
mov bx, 10 ===> BB0A00
Define Byte (8 bits)
Define word (16 bits)
Define double word (32 bits)
Define quadword (64 bits)
To refer to this variable later in the program, we need the address occupied by this variable. The assembler is there to help us. We can associate a symbol with any address that we want to remember and use that symbol in
the rest of the code. The symbol is there for our own comprehension of code. The symbol is known as label.
Label

## Slide 5
Chellenge Question
What should be the opcodes of the instructions in the red zone?
Check the opcodes in your lab work

## Slide 6
Using memory variables to write a better code

## Slide 7
The first instruction of our program has changed from B80500 to A11700.
The opcode B8 is used to move constants into AX, while the opcode A1 is used when moving data into AX from memory.
Lets take a closer look on the direct addressing
Insted of using four labels can we use one, just like we do in high-level languages?

## Slide 8
Rather than using four labels can we use one
Another way of writing it!!
Label is just an indication and num1 will be translated into a number.
Since dw is 2 bytes so we can also use num1+x to access data.

## Slide 9
Using memory to register for addressing
Program ended here and we can have data after that. (Logical window)
Memory location where we want our result.
Run this code on your simulator and see the com file on your debugger and see the change in the opcodes!!!

## Slide 10
Size Mismatch Issue
dw
Be careful about the data label and size of the data input

## Slide 11
Register Indirect Addressing
There are four registers in initial intel architecture that can hold address of data and they are BX, BP, SI, and DI. There are minute differences in their working which will be discussed later. For the current example, we will use the BX register.
Since num1 is not in square brackets it means it means only the address of the ``num1” will be moved to bx register not the contents of the num1.
Moving to next address that is two byte away in the memory
Now bx has the address of next word (10) in the num1:.
What if we want to add hundrad numbers instead of three numbers?
Ability to change address repeatedly
A way to repeat the “add” instruction 100 times.
Ability to change address repeatedly

## Slide 12
Register Indirect Addressing
What if we want to add hundrad numbers instead of three numbers?
Ability to change address repeatedly
A way to repeat the “add” instruction 100 times.
A way to repeat the “add” instruction 100 times and when to terminate the program.
JNZ (Jump if not zero)
Jump to the location defined by lable “l1” if the “ZERO FLAG” is not set.
“cx” register is used here as a counter.
“cx” contains the loop counter.

## Slide 13
Register + Offset Addressing
Combination of direct and indirect addressing