## Slide 1: Basic Computer Organization
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 processors”
Author “Kip R. Irvine”
6th Edition
Chapter 2
  Section 2.1

## Slide 3: Organization and Architecture
Computer Architecture
  Attributes of a computer that have a direct impact on the logical program execution
  e.g. I/O mechanisms, memory addressing techniques
Computer Organization
  Operational units and their interconnection that realizes the architectural specifications
  e.g. control signals, interconnection between computer and its peripherals

## Slide 4: Basic Computer Organization (1/2)
Computer has 3 main components
  Processor, also called Central Processing Unit (CPU)
  Memory and Storage Devices
  I/O Devices
These components communicate with each other through
  Data Bus
  I/O Bus
  Address Bus
  Control Bus

## Slide 5: Basic Computer Organization (2/2)
Memory Storage Unit
I/O Device #1
I/O Device #2
Central
Processing Unit
(CPU)
ALU | CU | CLOCK
I/O Bus
Address Bus
Control Bus
Registers
Data Bus

## Slide 6: Central Processing Unit (CPU)
Generally called Processor
Contains
  Clock
  Registers
  Arithmetic Logic Unit (ALU)
    Performs arithmetic and logic instructions
  Control Unit (CU)
    Generates the control signals required to execute the instructions

## Slide 7: Clock (1/2)
Clock cycle is basic unit of time for machine instructions
Synchronizes Processor and Bus operations
Clock cycle = Clock period = 1/(Clock Rate)
Clock Rate = Clock Frequency = Cycles per sec
  1 Hz clock produces 1 Clock Cycle in 1 second
  1 KHz clock produces 1000 Clock Cycles in 1 second
  1 MHz clock produces 1,000,000 cycles in 1 second
  1 GHz clock produces 1,000,000,000 cycles in 1 second

## Slide 8: Clock (2/2)
Clock Frequency | Clock Period (sec) | Time to execute one instruction
1 Hz | 1 | 1 sec
1 KHz | 0.001 | 1 ms (millisecond)
1 MHz | 0.000,001 | 1 μs (microsecond)
1 GHz | 0.000,000,001 | 1 ns (nanosecond)
1
0
One Cycle

## Slide 9: Memory (1/2)
Ordered sequence of bytes
  Sequence number is called memory address
Byte addressable memory
  Each byte has a unique address
Physical address space
  Determined by the address bus width
  Pentium has 32-bit address bus
    Physical address space of Pentium = 232 bytes = 4 GB
  Itanium with 64-bit address bus can support up to 264 bytes of physical address space

## Slide 10: Memory (2/2)
Address of location to be read/written is placed on the address bus
Data to be read/written is places on the data bus by memory/processor
Two control signals read and write decide the reading or writing operations
Memory Unit
Address
Read
Write
Data

## Slide 11: Physical Address Space
Address
in decimal
Address
in hex
0
1
2
232-1
00000000
00000001
00000002
FFFFFFFD
FFFFFFFE
FFFFFFFF
Address space is the set of addressable memory locations (bytes)

## Slide 12: Reading from Memory
Multiple clock cycles are required
Memory responds much more slowly than CPU
Reading process is carried out in this way
  Address is placed on the address bus
  Read Line (RL) goes low indicating that processor wants to read
  CPU waits for memory to respond
  Read Line (RL) goes high indicating that data has been placed on the data bus

## Slide 13: Memory Read and Write Cycles
In Read Cycle, the Processor
  places address on address bus
  asserts the memory read control signal
  waits for memory to place data on the data bus
  reads the data from data bus
  drops the memory read signal
In Write Cycle, the Processor
  places address on the address bus
  asserts the memory write control signal
  places the data on the data bus
  waits for memory to store the data
  drops the memory write signal

## Slide 14: Reading from Memory

## Slide 15: Memory Hierarchy
Registers
  Fastest storage elements
Cache Memory
  Stores recently used instructions
Main Memory
Magnetic Disk
  Stores data permanently
Magnetic Tape
Magnetic Tape
Magnetic Disk
CD-ROM
CD-RW
DVD-RW
Off-line Storage
Outboard
Storage
Inboard
Storage
Main Memory
Cache
Regis-ters
Lower cost per Byte
Higher Speed, Smaller Size

## Slide 16: Next Lecture
IA-32 Registers
  General Purpose Registers
  Special-Purpose and Segment Registers
  EFLAGS Registers