## Slide 1: Intel Architecture 32-bit (IA-32) Registers and Instruction Execution Cycle
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 processors”
Author “Kip R. Irvine”
6th Edition
Chapter 2
  Section 2.1.2
  Section 2.2

## Slide 3: Registers
Very high speed memory units inside CPU
Can be categorized into
  General Purpose Registers
  Segment Registers
  Instruction Pointer
  EFLAGS Register
    Control Flags
    Status Flags

## Slide 4: General Purpose Registers
Used primarily for arithmetic and data movement
Eight 32-bit Extended general purpose registers
Register | Description | Specialized Usage
EAX | Accumulator | Used in mul and div instruction
EBX | Base | 
ECX | Counter | Used in LOOP instruction
EDX | Data | 
EBP | Base Pointer | Used to reference local variables on stack
ESP | Stack Pointer | Points at top of the stack, used by PUSH and POP
ESI | Source Index | Used by high speed memory transfer instruction
EDI | Destination Index | Used by high speed memory transfer instruction

## Slide 5: Accessing Parts of Registers (1/2)
Portions of General Purpose Registers can also be accessed
  Lower 16 bits of EAX are named AX
  AX can further be divided into
    AL = Lower 8 bits
    AH = Higher 8 bits
EAX
AX
AH
AL
32 bits
16 bits
8 bits
0
7
8
15
16
31
8 bits

## Slide 6: Accessing Parts of Registers (2/2)
  EAX, EBX, ECX, EDX can be accessed at word and byte level
  EBP, ESP, ESI, EDI can be accessed at word level
32-bit | 16-bit | 8-bit Higher | 8-bit Lower
EAX | AX | AH | AL
EBX | BX | BH | BL
ECX | CX | CH | CL
EDX | DX | DH | DL
32-bit | 16-bit Lower
ESP | SP
EBP | BP
ESI | SI
EDI | DI

## Slide 7: Segment Registers (1/2)
Six 16-bit segment registers
Indicate base addresses of pre-assigned memory areas
An assembly program usually contains 3 segments
  Stack Segment: holds local function variables and function parameters
  Data Segment: holds variables
  Code Segment: holds program instructions

## Slide 8: Segment Registers (2/2)
SS = Stack Segment
DS = Data Segment
CS = Code Segment
3 extra segment registers
  ES, FS, GS (Extra Segment)
SS
DS
CS
ES
FS
GS

## Slide 9: Instruction Pointer
Represented by EIP
Also called Program Counter (PC)
Contains the address of next instruction to be executed
Its value changes with the execution of program
Certain machine instructions influence the value of EIP

## Slide 10: EFLAGS
EFLAGS register consists of individual binary bits
Can be categorized into
  Control Flags: control the operation of CPU
  Status Flags: reflect the outcome of arithmetic and logical operations
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ID | VIP | VIF | AC | VM | RF | 0 | NT | IOPL | OF | DF | IF | TF | SF | ZF | 0 | AF | 0 | PF | 1 | CF

## Slide 11: Status Flags
Arithmetic and Logical operations set/reset them
Status Flags are
  Carry Flag (CF): set when unsigned arithmetic operation produces a carry
  Overflow Flag (OF): sets when signed arithmetic result is out of range
  Sign Flag (SF): sets when result of operation is –ve
  Zero Flag (ZF): sets when result of operation is zero
  Auxiliary Flag (AF): sets when there is a carry from bit 3 to bit 4
  Parity Flag (PF): sets when parity is even

## Slide 12: Floating Point Unit (FPU)
FPU performs high speed floating point operations
Integrated into main processor chip from Intel486 onward
Eight 80-bit floating point data registers
All arranged as a stack
ST(7)
ST(1)
ST(0)
ST(3)
ST(2)
ST(5)
ST(4)
ST(6)

## Slide 13: Instruction Execution Cycle (1/2)
A program is loaded into memory before execution
Instruction Pointer (IP) contains the address of next instruction to be executed
Instruction Queue contains the group of instructions about to be executed
Three basic steps in execution of a machine instruction
  Fetch
  Decode
  Execute
Two more steps if the instruction uses an operand located in memory
  Fetch Operand
  Store Output

## Slide 14: Instruction Execution Cycle (2/2)
Order of steps when instruction uses an operand located in memory
  Instruction Fetch (IF)
  Instruction Decode (ID)
  Operand Fetch from Memory (OF)
  Instruction Execute (IE)
  Write Back in Memory (WB)
Instruction Execution Cycle (IEC) is the combination of all above operations

## Slide 15: Instruction Fetch
Program Counter (PC) or IP holds address of next instruction to be executed
Processor fetches instruction from memory pointed to be PC
Increment PC to the next instruction
Fetching operation concludes here

## Slide 16: Instruction Decode
Control Unit (CU) determines the function of the instruction
Instruction’s input operands are passed to ALU
Signals sent to ALU to perform the desired operation

## Slide 17: Operand Fetch from Memory
Sometimes instructions may involve some operands located in memory
In this case, data should be retrieved from memory
The CU uses a memory read operation
CU copies these operands into Instruction Registers which are invisible to user programs

## Slide 18: Instruction Execute
The instruction is ready for execution at this stage
ALU executes the instruction
ALU updates the status flags providing information about the result

## Slide 19: Write Back in Memory
The output may be required to save in memory for future uses
CU performs a write operation to save this output into memory

## Slide 20: IEC Graphical View
Instruction Fetch
Instruction Decode
Operand Fetch
Instruction Execute
Write Back in Memory
Obtain instruction from Instruction Queue
Determine required action to be executed
Locate and obtain operand from memory location
Compute the required operation
Deposit results in the storage for future use
Infinite Cycle

## Slide 21: Next Lecture
Overview of Intel Microprocessors
x86 Memory Management