## Slide 1: x86 Processor Architecture
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 processors”
Author “Kip R. Irvine”
6th Edition
Chapter 2
  Section 2.2.4
  Section 2.3

## Slide 3: Outline
Overview of Intel Microprocessors
x86 Memory Management

## Slide 4: Intel Microprocessors
Size of data bus is significant in processor evolution
How to transfer 32-bit data with an 8-bit data bus?

## Slide 5: Evolution of Intel Microprocessors (1/7)
Intel 8086
  16-bit registers and 16-bit data bus
  20-bit address bus
    Physical Address Space = 220 bytes = 1MB
Intel 8087
  Floating point co-processor
  Uses segmentation and real-address mode to address memory
  Each segment can address 216 bytes = 64 Kbytes
Intel 8088
  Uses 8-bit data bus
  … that’s why less expensive

## Slide 6: Evolution of Intel Microprocessors (2/7)
Intel 80286
  24-bit address bus so
    Physical Address Space = 224 bytes = 16 MB
Intel 80386
  First 32-bit processor with 32-bit general purpose registers
  32-bit data bus and 32-bit address bus so
    Physical Address Space = 232 bytes = 4GB

## Slide 7: Evolution of Intel Microprocessors (3/7)
Intel 80486, introduced in 1989
  Improved version of 80386
  On-chip Floating Point Unit
  On-chip unified Instruction/Data cache of 8 KB
  Introduced the concept of Pipelining
Pentium (80586), introduced in 1993
  32-bit address bus
  64-bit internal data path (inside a processor)
  Superscalar performance: can execute two instructions in one clock cycle
  Separate 8KB instruction and 8KB data caches

## Slide 8: Evolution of Intel Microprocessors (4/7)
Pentium Pro, introduced in 1995
  Three-way superscalar: can execute 3 instructions per clock cycle
  36-bit address bus  up to 64 GB of physical address space
  Introduced dynamic execution
    Out-of-order execution
  Integrated a 256 KB second level L2 cache on chip
Pentium II was introduced in 1997
  Added MMX instructions
Pentium III was introduced in 1999
  Added SSE instructions and eight new 128-bit XMM registers

## Slide 9: Evolution of Intel Microprocessors (5/7)
Pentium IV is a seventh generation x86 architecture
  New micro-architecture design called Intel Netburst
  Very deep instruction pipeline, scaling to very high frequencies
Intel introduced hyper-threading technology in 2002
  Allowed 2 programs to run simultaneously, sharing resources
Xeon is Intel’s name for its server-class microprocessors
  Xeon chips generally have more cache
  Support larger multiprocessor configurations

## Slide 10: Evolution of Intel Microprocessors (6/7)
Pentium M (Mobile) was introduced in 2003
  Designed for low-power laptop computers
  Modified version of Pentium III, optimized for power efficiency
  Large L2 cache
  Runs at lower clock than Pentium IV but with better performance
Extended Memory 64-bit Technology (EM64T)
  64-bit superset of the IA-32 processor architecture
  64-bit general purpose registers and integer support
  Number of general purpose registers increased from 8 to 64
  64-bit pointers and flat virtual address space
  Large physical address space: up to 240 = 1 Terabyte

## Slide 11: Evolution of Intel Microprocessors (7/7)
CISC – Complete Instruction Set Computer
  Large and complex instruction set
  Variable width instructions
  Requires microcode interpreter
  Example is Intel x86 family
RISC – Reduced Instruction Set Computer
  Small and simple instruction set
  All instructions have the same width
  Simpler instruction formats and addressing modes
  Decoded and executed directly by hardware
  Examples are ARM, MIPS, PowerPC, SPARC etc.

## Slide 12: Outline
Overview of Intel Microprocessors
x86 Memory Management

## Slide 13: x86 Operation Modes
x86 architecture operates in 3 basic different modes
  Protected Mode
    All instructions and features of processor are available
    Programs cannot reference memory outside their segments
    Virtual-8086 is special mode of Protected Mode
  Real-Address Mode
    Programs can have direct access to memory and hardware devices
    … so operating system can crash in this mode
  System Management Mode
    Implemented in processors customized for a particular system setup
    Supports power management and system security

## Slide 14: x86 Memory Management
Memory is managed according to the operation mode
  Real-Address Mode
  Protected Mode

## Slide 15: Real-Address Mode Memory Management
16-bit registers
20-bit address bus
  Physical Address Space = 1MByte
  Linear or Absolute Address range is 00000h to FFFFFh
How 20-bit address can be accommodated in 16-bit Registers?
  Solution lies in Segmented Memory

## Slide 16: Real-Address Mode Memory Management
Programs cannot use linear address directly because of 16-bit registers
Addresses are represented using 2 16-bit registers
  One 16-bit value is called Segment Value which is placed in segment register
  Other 16-bit value is called Offset value

## Slide 17: Segmented Memory Scheme
All memory is divided in 64KBytes segments
Each segment begins at an address having a zero in its last hex digit
  … this zero is omitted when representing segment value in 16-bit registers
    A segment value of E00016 refers to the segment address of E000016
If we have Physical Address Space of 220 bytes, and size of each segment is 64KBytes (216bytes), how many segments do we have?

## Slide 18: Segmented Memory Map
64 KBytes
00000
10000
20000
30000
40000
50000
7000:0000
7000:FFFF
Segment
Offset
017A
7000:017A
F0000
64 KBytes
60000
70000
80000
90000
A0000
B0000
C0000
D0000
E0000
Segment
Offset
7000:017A is called Logical Address
7017A is called Linear/Absolute Address

## Slide 19: 20-bit Linear Address Calculation
Segment value
0
15
Offset value
X
1016
+
20-bit Linear Address in hex
In Hex
In Hex
0
15
How to convert a 16-bitSeg:16-bitOffset logical address into 20-bit linear/absolute address

## Slide 20: Protected Mode Memory Management
Restricts application programs from accessing system hardware
Logical Address consists of
  16-bit segment selector (Segment Registers)
  32-bit offset value
Program’s linear address space is 4GBytes
  What is address bus width?
A typical protected-mode program has three segments
  Code Segment
  Data Segment
  Stack Segment
Segment Registers point to the Segment Descriptor Table
  … Segment Descriptor Tables are created by OS to keep track of individual program segments

## Slide 21: Paging
Paging divides the linear address space into fixed-sized block called pages
IA-32 uses pages of size 4 KB
Pages are allocated space on main memory
  … if main memory is full, then on hard disk
Complete set of pages mapped by OS is called Virtual Memory

## Slide 22: Paging
We want to run many programs in parallel
Main memory may not be enough to load all of them at the same time
Disk storage is cheaper and we have plenty of it
Paging gives an illusion that we have unlimited main memory
The more a program depends on paging, the slower it runs
Higher amount of main memory means less usage of paging