## Slide 1: Basics of Computer Organization
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 2
Chapter 3
  Section 3.1
  Section 3.2

## Slide 3: Architecture and Organization (1/2)
Architecture is those attributes visible to the programmer
  Instruction set, number of bits used for data representations, I/O mechanism, addressing techniques etc.
  e.g. is there an instruction for subtraction?
Organization is how features are implemented
  Control signals, interfaces, memory technology
  e.g. is there a hardware unit for subtractor or is it done by addition operations?

## Slide 4: Architecture and Organization (2/2)
All Intel x86 family share the same basic architecture
The IBM System/370 family share the same basic architecture
It gives backward code compatibility
Organization differs in different versions

## Slide 5: Outline
Computer Evolution and Performance
Von Neumann Architecture
A top level view of computer function
  Computer Components
Interconnection Structure
Bus Interconnection
Computer Memory System Overview

## Slide 6: Computer Evolution
Generation | Approximate Dates | Technology | Typical Speed (Operations/second)
1 | 1946 – 1957 | Vacuum tube | 40,000
2 | 1958 – 1964 | Transistor | 200,000
3 | 1965 – 1971 | Small and Medium Scale Integration | 1,000,000
4 | 1972 – 1977 | Large Scale Integration | 10,000,000
5 | 1978 – 1991 | Very Large Scale Integration | 100,000,000
6 | 1991 – | Ultra Large Scale Integration | 1,000,000,000
It is widely accepted to classify computers into generations based on the fundamental hardware technology employed

## Slide 7: Computer Evolution
First Generation of Computers
  Use of vacuum tubes
Second Generation of Computers
  Transistors replaced vacuum tubes
Third Generation of Computers
  Integrated Circuits were introduced
Later Generations
  Large Scale Integration (LSI)
  Very Large Scale Integration (VLSI)

## Slide 8: First Generation of Computers
Electronic Numerical Integrator And Computer (ENIAC) was first general purpose computer
Very expensive
  Weighted 30 tons
  Occupied 1500 square feet
  Contained more than 18000 vacuum tubes
  Consumed 140 kilowatts when operating
Used decimal system rather than binary system

## Slide 9: Outline
Computer Evolution and Performance
von Neumann Architecture
A top level view of computer function
  Computer Components

## Slide 10: von Neumann Architecture
ENIAC did not provide the facility to store programs
Stored-Program Concept proposed by John von Neumann
Much similar to modern machines
  …that’s why today’s computers are referred to as Von Neumann Machines

## Slide 11: IAS Computer (1/2)
Followed stored-program concept
It contained
  Main memory storing programs and data
  ALU operating on binary data
  Control Unit interprets instructions from memory and causes them to be executed
  Input and Output equipment operated by control unit

## Slide 12: IAS Computer (2/2)
Main Memory (M)
I/O Equipment (I,O)
Arithmetic Logic Unit (CA)
Program Control Unit (CC)
Central Processing Unit (CPU)

## Slide 13: IAS Details
1000 words each of 40 bits
  Binary Numbers
  2x20 bit instructions
Set of registers (storage in CPU)
  Memory Buffer Register (MBR)
  Memory Address Register (MAR)
  Instruction Register (IR)
  Instruction Buffer Register (IBR)
  Program Counter (PC)
  Accumulator (AC)
  Multiplier Quotient (MQ)

## Slide 14: IAS Expanded Structure
I/O Equipment
Main Memory
AC
MQ
Arithmetic-logic circuits
MBR
IBR
PC
IR
MAR
Control circuits
Arithmetic Logic Unit (ALU)
Program Control Unit

## Slide 15: Outline
Computer Evolution and Performance
von Neumann Architecture
A top level view of computer function
  Computer Components

## Slide 16: Computer Components
According to von Neumann machine architecture, a computer has the following components
  Central Processing Unit (CPU)
  Main Memory
  I/O Components
A top level view of computer components is shown in next slide

## Slide 17: Computer Components
MAR
MBR
I/O AR
I/O BR
PC
IR
Execution Unit
CPU
I/O Module
Buffers
Main Memory
0
1
2
n-1
n-2
Data
Data
Data
Data
Instruction
Instruction
Instruction
Instruction

## Slide 18: Interrupts
Mechanism by which other modules may interrupt normal sequence of processing
If normal execution of current program must be interrupted, the device raises an interrupt signal
Interrupt-service routine
Current system information is backed up before calling interrupt handler
After interrupt completion, the previous system information is restored

## Slide 19: Classes of Interrupts
4 different classes of interrupts
Program
  Generated by program executions
  Arithmetic overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  From I/O controller
Hardware failure
  Power failure, memory parity error

## Slide 20: Interrupt Cycle
Added to instruction execution cycle
Processor checks for interrupts
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending…
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 21: Instruction Execution Cycle with Interrupts
Fetch next Instruction
Execute Instruction
Check for Interrupts; process interrupt
START
HALT
Fetch Cycle
Execute Cycle
Interrupt Cycle
Interrupts disabled
Interrupts enabled

## Slide 22: Transfer of Control via Interrupts
1
2
i
i+1
M
M-1
Interrupt occurs here
User Program
Interrupt Handler

## Slide 23: Multiple Interrupts
Multiple interrupts can occur in some situations
Multiple interrupts can be handled using two approaches
  Disabling Interrupts
  Defining properties of interrupts

## Slide 24: Disabling Interrupts
Processor can ignore further interrupts whilst processing one interrupt
Interrupts remain pending and are checked after first interrupt has been processed
Interrupts are handled in sequence as they occur hence called Sequential Interrupts
User Program
Interrupt Handler X
Interrupt Handler Y

## Slide 25: Defining Properties of Interrupts
Low priority interrupts can be interrupted by higher priority interrupts
When higher priority interrupt has been processed, processor returns to previous interrupt
These types of interrupts are called Nested Interrupts
User Program
Interrupt Handler X
Interrupt Handler Y