## Slide 1: Interconnection Structures
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 3
  Section 3.3
  Section 3.4

## Slide 3: Interconnection Structures
Three basic computer components
  Processor
  Main memory
  I/O Devices
They need to interact with each other to perform their functions
Collection of paths connecting above modules is called Interconnection Structures
Type of connection depends upon the module
  Memory Connection
  I/O Module Connection
  CPU Connection

## Slide 4: Memory Connection
Receives and send data
Receives addresses of memory locations
Receives control signals
  Read
  Write
  Timing

## Slide 5: I/O Module Connection
Similar to memory from computer’s viewpoint
Input connection
  Receives data from peripheral
  Sends data to computer
Output connection
  Receives data from computer
  Sends data to peripheral

## Slide 6: CPU Connection
Reads instructions and data
Writes out data after processing
Sends control signals to other units
Receives and acts on interrupts

## Slide 7: Bus Interconnection
A Bus is a communication path connecting two or more devices
Each bus consists of single/multiple lines
Bus that connects major computer components like processor, memory and I/O, is called System Bus
Bus lines can be classified into three different types depending upon their functionality
  Data Lines
  Address Lines
  Control Lines

## Slide 8: Data Lines
Used to move data between system modules
Called Data Bus altogether
Carries data
  Remember that there is not any difference between “data” and “instruction” at this level
  Width is a key determinant of performance
    32, 64 or 128 data lines
Number of lines is equal to the number of bits transferred at one time

## Slide 9: Address Lines
Identify the source or destination of data
  e.g. CPU needs to read an instruction from a given location in memory
Bus width determines maximum memory capacity of system

## Slide 10: Control Lines
Control the use of data and address lines
Used to transmit command and timing signals
Timing signals indicate the validity of data and address information
Command signals specify operation to be executed
Typical control signals include
  Memory read/write signal
  Interrupt request
  Clock signal

## Slide 11: Bus Interconnection Scheme

## Slide 12: Speed Issues
Different devices have different transfer/operate speed
If the speed of bus is bounded by the slowest device connected to it, the efficiency will be very low
How to solve it?
  A common approach is using buffers

## Slide 13: Single Bus Problems
Lots of devices on one bus leads to
  Propagation delay
    Long data paths mean that coordination of bus use can adversely affect performance
    Aggregate data transfer approaches bus capacity
Most systems use multiple buses to overcome these problems

## Slide 14: Bus Types
Dedicated Bus
  Permanently assigned one function
  Separate Data and Address lines
Multiplexed Bus
  Shares lines
  Address valid or Data valid control line
  Advantage – fewer lines
  Disadvantage
    More complex circuitry
    Potential reduction in performance

## Slide 15: Bus Arbitration
More than one modules may need control of the bus
Only one unit at a time can successfully transmit over the bus
Arbitration may be
  Centralized
    Single hardware device controlling the bus access
  Distributed
    Each module may claim the bus
    Control logic on all modules

## Slide 16: Timing
Coordination of events on bus
Synchronous
  Events determined by clock signals
  Control Bus includes clock line
  All devices can read clock line
  Usually a single cycle for an event

## Slide 17: Synchronous Timing Diagram

## Slide 18: Asynchronous Timing Diagram
System bus read cycle

## Slide 19: Asynchronous Timing Diagram
System bus write cycle

## Slide 20: Synchronous vs. Asynchronous
Synchronous timing is simpler to implement
Less flexible than asynchronous timing
Because all devices on synchronous bus are tied to a fixed clock rate, the system cannot take advantage of advances in device performance
With asynchronous timing, a mixture of slow and fast devices, using older and newer technology, can share a bus