## Slide 1: Defining Data
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 3
  Section 3.4

## Slide 3: Data Definition Statement (1/2)
Assigns storage in memory for a variable
Syntax for a data definition statement is
Name is optional and must follow the rules of naming the identifiers
At least one initializer is required
Question mark (?) can be used as initializer if uninitialized variable
[name] directive initializer [,initializer]

## Slide 4: Data Definition Statement (2/2)
Directive can be any of the following
Directive | Description | Usage
DB | Define Byte | 8-bit Integer
DW | Define Word | 16-bit Integer
DD | Define Doubleword | 32-bit Integer
DQ | Define Quadword | 64-bit Integer
DT | Define Tenbytes | 80-bit Integer

## Slide 5: DB Directive
Defines an 8-bit signed or unsigned variable
The initializer must fit into 8-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DB 255 ; largest unsigned value
  val2 DB +127 ; largest signed value
[name] DB initializer

## Slide 6: DW Directive
Defines a 16-bit signed or unsigned integer
The initializer must fit into 16-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DW 65535 ;largest unsigned value
  val2 DW -32768 ;smallest signed value
[name] DW initializer

## Slide 7: DD Directive
Defines a 32-bit signed or unsigned integer
The initializer must fit into 32-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DD FFFFFFFFh ;largest unsigned value
  val2 DD 80000000h ;smallest signed value
[name] DD initializer

## Slide 8: DQ Directive
Defines a 64-bit signed or unsigned integer
The initializer must fit into 64-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DQ 10001010h
  val2 DQ 10001010b
[name] DQ initializer

## Slide 9: Multiple Initializers
If multiple initializers are used in the same data definition statement
  … its label refers only to the offset of first initializer
Also called Array
Example is
  vals1 DB 10, -20, 30
  vals2 DW 0Ah, 10, 00111100b
[name] Directive initializer ,initializer

## Slide 10: Defining Strings
Strings are sequence of characters including spaces
Enclosed in single or double quotation marks
As they are sequence of characters and each character occupies 1 byte, DB directive is used to define them
End with a null byte
Examples are
  str1 DB “Hello”, 0
  str2 DB ‘Hello’, 0

## Slide 11: DUP Operator
DUPlicates same value on many storage locations
Useful when allocating space for string or array
Can be used with initialized or uninitialized data
Examples are
  a DB 10 DUP(0) ;10 bytes all zero
  b DB 10 DUP(?) ;10 bytes uninitialized
  c DB 3 DUP (‘hi’);6 bytes ‘hihihi’

## Slide 12: Defining Real Number Data
DD, DQ, DT directives can be used to define real numbers
Examples are
  rVal1 DD 1.2
  rVal2 DQ 3.1E-190
  rVal3 DT 8.9E+3036
Data Type | Significant Digits | Approximate Range
DD (Short Real) | 6 | 1.18x10-38 to 3.40x1038
DQ (Long Real) | 15 | 2.23x10-308 to 1.79x10308
DT (Extended-precision Real) | 19 | 3.37x10-4932 to 1.18x104932

## Slide 13: Little Endian Order
x86 processors store and retrieve data from memory using Little Endian Order
Least significant byte is stored at the first memory address allocated for data
Remaining bytes are stored in the next consecutive memory locations
Example, consider 2-bytes value 1234h
  If placed in memory at offset 0000, 34h would be stored in first byte
  12h would be stored in the second byte

## Slide 14: Big Endian Order
Some other processors store and retrieve data from memory using Big Endian Order
Most significant byte is stored at the first memory address allocated for data
Remaining bytes are stored in the next consecutive memory locations
Example, consider 2-bytes value 1234h
  If placed in memory at offset 0000, 12h would be stored in first byte
  34h would be stored in the second byte