## Slide 1: Addition and Subtraction
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 4
  Section 4.2

## Slide 3: Outline
INC and DEC Instructions
ADD Instruction
SUB Instruction
NEG Instruction
FLAGS affected by Addition and Subtraction

## Slide 4: INC and DEC Instructions (1/2)
INC instruction increments 1 in a single operand
DEC instruction decrements 1 from a single operand
Syntax is
  INC reg/mem
  DEC reg/mem
Flags affected
  OF, SF, ZF, AF, PF

## Slide 5: INC and DEC Instructions (2/2)
.data
a DB 10h
.code
INC a
MOV al, a
DEC al
a = 11h
al = 10h

## Slide 6: ADD Instruction
Adds a source operand into a destination operand
Both operands must have the same size
Sum is stored in the destination operand
Syntax is
Flags affected
  CF, ZF, SF, OF, AF, PF
ADD dest, src

## Slide 7: SUB Instruction
Subtracts a source operand from a destination operand
Both operands must have the same size
Result is stored in the destination operand
Syntax is
Flags affected
  CF, ZF, SF, OF, AF, PF
SUB dest, src

## Slide 8: NEG Instruction
Reverses the sign of a number by taking its 2’s complement
Syntax is
  NEG reg
  NEG mem
Flags affected
  CF, ZF, SF, OF, AF, PF

## Slide 9: Flags Affected by Addition and Subtraction
Status flags reflect the outcome of an arithmetic or logic instruction
  … based on the contents of destination operand
Essential flags are
  ZF: set when destination operand equals zero
  SF: set when destination operand is negative
  CF: set when unsigned value is out of range
  OF: set when signed value is out of range
MOV instruction never affects the flags

## Slide 10: Zero Flag (ZF)
ZF is set when the result of an operation produces zero in the destination operand
Remember that
  A flag is set when it equals 1
  A flag is clear when it equals 0
MOV al, 1
SUB al, 1
MOV bl, 0FFh
INC bl
INC bl
;no flag affected
;al=0  ZF=1
;no flag affected
;bl=0  ZF=1
;bl=1  ZF=0

## Slide 11: Sign Flag (SF)
SF is set when destination operand is –ve
SF is clear when destination is +ve
MOV al, 0
SUB al, 1
ADD al, 2
;no flag affected
;al=-1  SF=1
;al=1  SF=0

## Slide 12: Carry Flag (CF)
CF is set when result of an arithmetic operation generates an unsigned value that cannot fit into destination operand
MOV al, 0FFh
ADD al, 1
MOV al, 0
SUB al, 1
;no flag affected
;al=00h  CF=1
;no flag affected
;al=0FFh  CF=1

## Slide 13: Overflow Flag (OF) (1/2)
OF is set when the result of a signed arithmetic operation overflows or underflows the destination operand
MOV al, +127
ADD al, 1
MOV al, -128
SUB al, 1
;no flag affected
;al=??  OF=1
;no flag affected
;al=??  OF=1

## Slide 14: Overflow Flag (OF) (2/2)
When adding two integers, remember that OF is only set when
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive