## Slide 1: Conditional Processing
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 6
  Section 6.1
  Section 6.3

## Slide 3: Boolean and Comparison Instructions
Four basic Boolean operations
  AND
  OR
  XOR
  NOT
Boolean operations can be carried out at bit-level

## Slide 4: AND Instruction (1/2)
Performs a bitwise AND operation between matching bits in two operands
Syntax is AND dest, src
The permitted operand combinations are
  AND reg, reg
  AND reg, mem
  AND reg, imm
  AND mem, reg
  AND mem, imm
x | y | x^y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5: AND Instruction (2/2)
Can be used for bit masking
  ... We can clear certain bits from a value by ANDing those bits with 0
Difference of only 1 bit (bit number 5) in lower case and upper case alphabets
  By ANDing any smaller alphabet with 11011111, it can be converted to upper case
Always clears OF and CF
Modifies SF, ZF, PF

## Slide 6: OR Instruction (1/2)
Performs a Boolean OR operation between matching bits of two operands
Syntax is OR dest, src
Permitted operand combinations are same as of AND
  OR reg, reg
  OR reg, mem
  OR reg, imm
  OR mem, reg
  OR mem, imm
x | y | x OR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7: OR Instruction (2/2)
Useful when we need to set one or more bits in an operand without affecting other bits
Always clears OF and CF
Modifies the values of SF, ZF and PF
If a number is ORed with itself, values of ZF and SF indicate following information
ZF | SF | Value of operand is …
Clear | Clear | Greater than zero
Set | Clear | Equal to zero
Clear | Set | Less than zero

## Slide 8: XOR Instruction (1/2)
Performs a Boolean exclusive-OR between matching bits in two operands
Syntax is XOR dest, src
Operand combinations are same as of AND and OR
  XOR reg, reg
  XOR reg, mem
  XOR reg, imm
  XOR mem, reg
  XOR mem, imm
x | y | x  y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9: XOR Instruction (2/2)
A bit XORed with 0 retains its value, and a bit XORed with 1 is toggled
XOR reverses itself when applied twice to the same operand
  This property makes XOR ideal for a simple form of symmetric encryption
Always clears OF and CF
Modifies SF, ZF and PF

## Slide 10: NOT Instruction
Toggles all bits in an operand
Result is called one’s complement
NOT takes only one operand with following formats
  NOT reg
  NOT mem
NOT does not affect any flags

## Slide 11: CMP Instruction (1/2)
Comparison is performed to replicate conditional branching/loops
CMP instruction performs an implied subtraction of a source operand from a destination operand
Neither operand is changed
Syntax is CMP dest, src
Uses the same operand combinations as of AND and OR
CMP instruction affects the flags in following way
  Changes OF, SF, ZF, CF, AF and PF

## Slide 12: CMP Instruction (2/2)
when compared two unsigned operands
When compared two signed operands then
CMP Results | ZF | CF
Dest < Src | 0 | 1
Dest > Src | 0 | 0
Dest = Src | 1 | 0
CMP Results | Flags
Dest < Src | SF ≠ OF
Dest > Src | SF = OF
Dest = Src | ZF = 1

## Slide 13: Setting/Clearing Individual Flags
Zero Flag (ZF)
  To set, AND an operand with 0
  To clear, OR an operand with 1
Sign Flag (SF)
  To set, OR MSB of an operand with 1
  To clear, AND MSB of an operand with 0
Carry Flag (CF)
  To set, use STC instruction
  To clear, use CLC instruction
Overflow Flag (OF)
  To set, add two positive values that produce negative sum
  To clear, OR an operand with 0

## Slide 14: Conditional Jumps (1/2)
No high-level logic structures such as if-then-else in IA-32 instruction set
In assembly language, a combination of comparisons and jumps can be used to implement any logic structure
First, an operation such as CMP, AND or SUB etc. modifies the status flags
Second, a conditional jump instruction tests the flags and causes a branch to new address

## Slide 15: Conditional Jumps (2/2)
Example 1
CMP al, 0
JZ L1 ;jump if ZF=1
.
.
.
L1:
.
.
Example 1
CMP al, 0
JNZ L1 ;jump if ZF=0
.
.
.
L1:
.
.

## Slide 16: JCOND Instruction
A conditional jump instruction branches to a destination label when a status flag condition is true
If the flag condition is false, the instruction immediately after the conditional jump is executed
Syntax is JCOND dest
COND refers to a flag identifying the state of one or more flags

## Slide 17: How to Use Conditional Jump?
First an arithmetic/logic operation is performed
After this operation, status flags in EFLAGS register are set/cleared
Now jump instruction can be performed based upon the value of flags

## Slide 18: Types of Conditional Jump Instructions
The conditional jump instructions can be divided into four groups
  Jumps based on specific flag values
  Jumps based on equality between operands or the value of CX
  Jumps based on comparisons of unsigned operands
  Jumps based on comparisons of signed operands

## Slide 19: Jumps Based on Flag Values
Mnemonic | Description | Flags/Registers
JZ | Jump if Zero | ZF = 1
JNZ | Jump if Not Zero | ZF = 0
JC | Jump if Carry | CF = 1
JNC | Jump if Not Carry | CF = 0
JO | Jump if Overflow | OF = 1
JNO | Jump if Not Overflow | OF = 0
JS | Jump if Signed | SF = 1
JNS | Jump if Not Signed | SF = 0
JP | Jump if Parity | PF = 1
JNP | Jump if Not Parity | PF = 0

## Slide 20: Jumps Based on Equality
Jumps based on equality are taken either
  Two operands are compared with CMP instruction or
  Based on the value of CX or ECX
Mnemonic | Description
JE | Jump if Equal
JNE | Jump if Not Equal
JCXZ | Jump if CX = 0
JECXZ | Jump if ECX = 0

## Slide 21: Jumps Based on Unsigned Comparisons
Mnemonic | Description
JA | Jump if Above (if dest > src)
JNBE | Jump if Not Below or Equal (same as JA)
JAE | Jump if Above or Equal (if dest ≥ src)
JNB | Jump if Not Below (same as JAE)
JB | Jump if Below (if dest < src)
JNAE | Jump if Not Above or Equal (same as JB)
JBE | Jump if Below or Equal (if dest ≤ src)
JNA | Jump if Not Above (same as JBE)
CMP unsigned_dest, unsigned_src
Junsigned

## Slide 22: Jumps Based on Signed Comparisons
Mnemonic | Description
JG | Jump if Greater (if dest > src)
JNLE | Jump if Not Less than or Equal (same as JG)
JGE | Jump if Greater than or Equal (if dest ≥ src)
JNL | Jump if Not Less (same as JGE)
JL | Jump if Less (if dest < src)
JNGE | Jump if Not Greater than or Equal (same as JL)
JLE | Jump if Less than or Equal (if dest ≤ src)
JNG | Jump if Not Greater (same as JLE)
CMP signed_dest, signed_src
Jsigned

## Slide 23: Conditional Loop Instructions (1/2)
LOOPZ (LOOP if Zero)
  Works just like LOOP with one additional condition that ZF must be set in order to transfer control to destination label
LOOPE (LOOP if Equal)
  Equivalent to LOOPZ
LOOPZ and LOOPE perform the following tasks when executed
  ECX = ECX – 1
  If ECX > 0 and ZF = 1, jump to destination

## Slide 24: Conditional Loop Instructions (2/2)
LOOPNZ (LOOP if Not Zero)
  Counterpart of LOOPZ
LOOPNE (LOOP if Not Equal)
  Same as LOOPNZ
LOOPNZ and LOOPNE perform the following tasks when executed
  ECX = ECX – 1
  If ECX > 0 and ZF = 0, jump to destination