## Slide 1: Stack Operations
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 5
  Section 5.4

## Slide 3: Stack
A LIFO (Last In First Out) data structure
New value is added to the top of stack
Existing values are removed from the top of stack
An essential part of calling from and returning to the procedures
Real life example
  A stack of plates

## Slide 4: Runtime Stack (1/3)
A memory array managed by CPU using ESP/SP (Extended Stack Pointer) register and SS (Stack Segment)
ESP/SP always points to the last value pushed on the top of stack and holds offset of that value in Stack Segment
ESP/SP cannot be manipulated directly instead it can be modified indirectly by instructions such as PUSH, POP, CALL, RET

## Slide 5: Runtime Stack (2/3)
In protected mode i.e. 32-bit mode, size of each stack location is 32-bits
In real-address mode i.e. 16-bit mode, size of each stack location is 16-bits
emu8086 uses real-address mode
Runtime Stack is different from Stack Abstract Data Type which is typically written in a HLL

## Slide 6: Runtime Stack (3/3)
SS contains the base address of Stack Segment
SP contains the offset of value at the top of stack
0700:FFF0
0700:FFF2
0700:FFF4
0700:FFF6
0700:FFF8
0700:FFFA
0700:FFFC
0700:FFFE
16-bits
SP
Segment:Offset
000A

## Slide 7: Push Operation (1/3)
A push operation in stack puts the value on the top location available in stack and decrements the stack pointer by size of stack element
Size of each stack element is 32 bits in protected address mode
Size of each stack element is 16 bits in real-address mode

## Slide 8: Push Operation (2/3)
0700:FFF0
0700:FFF2
0700:FFF4
0700:FFF6
0700:FFF8
0700:FFFA
0700:FFFC
0700:FFFE
000A
SP
Before
0700:FFF0
0700:FFF2
0700:FFF4
0700:FFF6
0700:FFF8
0700:FFFA
0700:FFFC
0700:FFFE
000A
SP
After
1000
2000
3000
SP is decremented by 2 with each push operation
These values are pushed on stack
  1000h
  2000h
  3000h

## Slide 9: Push Operation (3/3)
0700:FFF0
0700:FFF2
0700:FFF4
0700:FFF6
0700:FFF8
0700:FFFA
0700:FFFC
0700:FFFE
000A
This value is pushed on stack
1000 0000h
ERROR
SP

## Slide 10: Pop Operation
Removes value from top of stack
SP is incremented by stack element size with each pop operation
0700:FFF0
0700:FFF2
0700:FFF4
0700:FFF6
0700:FFF8
0700:FFFA
0700:FFFC
0700:FFFE
000A
SP
Before
1000
2000
3000
0700:FFF0
0700:FFF2
0700:FFF4
0700:FFF6
0700:FFF8
0700:FFFA
0700:FFFC
0700:FFFE
000A
SP
After
1000
2000
16-bits

## Slide 11: PUSH Instruction
PUSH instruction is executed in two steps
  First decrements SP by the size of stack element
  Then copies the source operand on top of stack
PUSH instruction formats
  PUSH reg/mem16  contents of 16-bit register or 16-bit memory location is pushed on stack
  PUSH imm16  16-bit immediate value is pushed on stack
Examples are
  PUSH AX
  PUSH 10h

## Slide 12: POP Instruction
POP instruction is executed in two steps
  First the contents of stack element pointed to by SP are copied into destination operand
  Then SP is incremented by the size of stack element
Only one POP instruction formats
  POP reg/mem16  copies the value pointed to by SP into 16-bit register or 16-bit memory location
Examples are
  POP AX
  POP var ;where var is a 16-bit memory location

## Slide 13: PUSHF and POPF Instructions
PUSHF is used to push EFLAGS register on the stack
POPF pops the stack into EFLAGS register
When using these instructions, make sure program’s execution path does not skip over POPF instruction
Syntax is
  PUSHF
  POPF

## Slide 14: PUSHA and POPA Instructions
PUSHA instruction pushes all 16-bit general purpose register on the stack in given order
  AX, CX, DX, BX, SP, BP, SI, DI
POPA instruction pops the same registers in the revers order
Useful when modifying many general purpose registers inside a procedure

## Slide 15: Stack Applications
Registers can be saved temporarily when used for more than one purpose
When CALL instruction executed, return address is saved on the stack
Arguments are passed to a subroutine by pushing them on the stack
Stack can be used as temporary storage for local variables inside a subroutine