## Slide 1: Shift and Rotate Instructions
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 7
  Section 7.2

## Slide 3: Shift and Rotate Instructions (1/2)
Shifting an operand means moving bits right or left from their original positions inside the operand
Rotating an operand fills the bit positions of empty end with the bits gone out on the other end of operand
Shift and Rotate instructions affect the Carry and Overflow flags
Two ways to shift an operand’s bits
  Logical Shift
  Arithmetic Shift

## Slide 4: Logical Shift
Fills the newly created bit positions with zero
Each bit value is shifted to left or right bit position
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
Logical Shift Right
by 1 position
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
CF
1

## Slide 5: Arithmetic Shift
Newly created bit is filled with a copy of sign-bit
Preserves the number’s sign-bit
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
Arithmetic Shift Right
by 1 position
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
CF
1

## Slide 6: Shift and Rotate Instructions (2/2)
Instruction Mnemonic | Description
SHL | Shift Left
SHR | Shift Right
SAL | Shift Arithmetic Left
SAR | Shift Arithmetic Right
ROL | Rotate Left
ROR | Rotate Right
RCL | Rotate Carry left
RCR | Rotate Carry Right
SHLD | Double-precision Shift Left
SHRD | Double-precision Shift Right

## Slide 7: SHL Instructions
Performs a logical shift left on the destination operand
Syntax for SHL is
  SHL dest, count
CF
0
SHL reg, imm8
SHL mem, imm8
SHL reg, CL
SHL mem, CL
Same for all shift and rotate instructions

## Slide 8: Fast Multiplication
Shifting left by 1 position generates a number which is 2 times the original operand
Shift left by n position multiplies the operand by 2n
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Before
SHL by 1 position
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 9: SHR Instructions
Performs a logical shift right on the destination operand
Highest bit position are filled with zero
Syntax for SHL is
  SHR dest, count
CF
0

## Slide 10: SAL and SAR Instructions
SAL is identical to SHL
SAR performs a right arithmetic shift on the destination operand
CF

## Slide 11: ROL Instructions
Shifts each bit to the left
The highest bit is copied into the CF and into the lowest bit
No bits are lost
CF

## Slide 12: ROR Instructions
Shifts each bit to the right
The lowest bit is copied into the CF and into the highest bit
No bits are lost
CF

## Slide 13: RCL Instruction
Shifts each bit to the left
Copies the carry flag to the LSB
Copies the MSB into carry flag
CF

## Slide 14: RCR Instruction
Shifts each bit to the right
Copies the carry flag to the MSB
Copies the LSB to the carry flag
CF

## Slide 15: SHLD Instruction
Shifts destination operand a give number of bits to left
Bit positions opened up by the shift are filled by the most significant bits of the source operand
Source operand is not affected
Syntax is
Operand Types
SHLD dest, src, count
SHLD reg16/32, reg16/32, imm8/CL
SHLD mem16/32, reg16/32, imm8/CL

## Slide 16: SHRD Instruction
Shifts destination operand a given number of bits to the right
Bit positions opened up by the shift are filled by the least significant bits of the source operand
Source operand is not affected
Syntax is
Operand Types
SHRD dest, src, count
SHRD reg16/32, reg16/32, imm8/CL
SHRD mem16/32, reg16/32, imm8/CL