## Slide 1: Multiplication and Division Instructions
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 7
  Section 7.4

## Slide 3: Integer Multiplication
Integer multiplication in x86 can be performed as a 32-bit, 16-bit or 8-bit operation
The default destination operand in these instructions is the accumulator register (EAX/AX/AL)

## Slide 4: MUL Instruction (1/2)
Used to multiply unsigned numbers
The multiplier and multiplicand must be the same size and product is twice their size
MUL instruction has a single operand which is multiplier
MUL reg/mem8 ;AX = AL * 8-bit reg/mem
MUL reg/mem16 ;DX:AX = AX * 16-bit reg/mem
MUL reg/mem32 ;EDX:EAX = EAX * 32-bit reg/mem

## Slide 5: MUL Instruction (2/2)
Multiplicand | Multiplier | Product
AL | 8-bit reg/mem | AX
AX | 16-bit reg/mem | DX:AX
EAX | 32-bit reg/mem | EDX:EAX
MUL sets the CF and OF if upper half of product is non-zero
When AL is multiplied with an 8-bit value, CF and OF are set if AH is non-zero

## Slide 6: IMUL Instruction
Used to multiply signed numbers
Preserves sign by extending highest bit of lower half of the product into the upper bits of product
Three formats of the IMUL instruction
  One-operand format
  Two-operand format
  Three-operand format
IMUL reg/mem ;AX = AL * reg/mem
IMUL reg, reg/mem ;AX = reg * reg/mem
IMUL reg, reg/mem, imm ;reg = reg/mem * imm

## Slide 7: DIV Instruction
Used to divide unsigned integers
Performs 8-bit, 16-bit and 32-bit integer division
Takes only one operand which is the divisor
DIV reg/mem8
DIV reg/mem16
DIV reg/mem32
Dividend | Divisor | Quotient | Remainder
AX | 8-bit reg/mem | AL | AH
DX:AX | 16-bit reg/mem | AX | DX
EDX:EAX | 32-bit reg/mem | EAX | EDX

## Slide 8: IDIV Instruction
Used to divide signed numbers
Uses same operand types as DIV instruction
Before executing 8-bit division, the dividend (AX) must be completely sign-extended using
  CBW (Convert Byte to Word)
  CWD (Convert Word to Double-word)
  CDQ (Convert Double-word to Quad-word)
Remainder has the same size as dividend

## Slide 9: Sign Extension Instructions
CBW
  Extends the sign-bit of AL into AH
CWD
  Extends the sign-bit of AX into DX
CDQ
  Extends the sign-bit of EAX into EDX
MOV AL, -8 ;AL=1111 1000
CBW ;AX=1111 1111 1111 1000
MOV AX, -8 ; AX=1111 1111 1111 1000
CWD ; AX=1111 1111 1111 1000
; DX=1111 1111 1111 1111

## Slide 10: Extended Addition and Subtraction
Extended precision addition/subtraction helps add/subtract numbers having almost unlimited size
ADC helps to add two numbers using the carry flag
SBB helps to subtract two numbers using borrow from carry flag

## Slide 11: ADC Instruction
Adds both a source operand and the value of CF to a destination operand
Instruction format and limitations are same as that of ADD instruction
MOV DL, 0
MOV AL, 0FFh
ADD AL, 0FFh ;AL=FEh, CF=1
ADC DL, 0 ;DL/AL=01FEh

## Slide 12: SBB Instruction
Subtracts both a source operand and value of CF from a destination operand
Possible operands are same as for the SUB instruction
MOV AH, 7
MOV AL, 1
SUB AL, 2 ;AL=FFh, CF=1
SBB AH, 0 ;AH/AL=06FFh