## Slide 1: String Representation
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 9
  Section 9.2

## Slide 3: String Instructions (1/2)
Five groups of instructions for processing array of Bytes, Words and Double-words
Called String Primitives but not limited to character arrays only
These instructions use ESI/SI and EDI/DI registers to address memory
Array indexes are repeated and incremented automatically

## Slide 4: String Instructions (2/2)
Instruction | Description
MOVSB, MOVSW, MOVSD | Copy data from memory addressed by SI to memory addressed by DI
CMPSB, CMPSW, CMPSD | Compare the contents of memory addressed by SI to memory addressed by DI
SCASB, SCASW, SCASD | Compare the accumulator register (AL, AX or EAX) to the contents of memory addressed by DI
STOSB, STOSW, STOSD | Store the contents of accumulator register into memory location addressed by DI
LODSB, LODSW, LODSD | Load the contents of memory addressed by SI into the accumulator register

## Slide 5: Direction Flag
String instructions increment/decrement SI and DI based on the state of Direction Flag
DF can be explicitly modified using instructions
  CLD ;clear Direction Flag (forward direction)
  STD ;set Direction Flag (reverse direction)
Value of DF | Effect on SI and DI | Address Sequence
Clear | Increment | Low-High
Set | Decrement | High-Low
if(DF=0) then
SI=SI+1
DI=DI+1
else
SI=SI-1
DI=DI-1
end if

## Slide 6: Repeat Prefix
REP (a repeat prefix) can be used just before MOVSB, MOVSW, MOVSD
By default CX controls the number of repetitions
Prefix | Description
REP | Repeat while CX>0
REPZ, REPE | Repeat while ZF=1 and CX>0
REPNZ, REPNE | Repeat while ZF=0 and CX>0

## Slide 7: REP Prefix
Repeat while CX>0
Value of CX is checked before execution of instruction
If CX is zero, string instruction is not executed
while(CX≠0)
execute the string instruction
CX = CX – 1
end while

## Slide 8: REPE, REPZ Prefixes
while(CX≠0)
execute the string instruction
CX = CX – 1
if (ZF=1) then
exit loop
end if
end while

## Slide 9: REPNE, REPNZ Prefixes
while(CX≠0)
execute the string instruction
CX = CX – 1
if (ZF=0) then
exit loop
end if
end while

## Slide 10: MOVSB, MOVSW, MOVSD (1/2)
Copy data from memory location pointed to by SI to memory location pointed to by DI
SI and DI are either incremented or decremented based on the value of DF
SI/DI incremented/decremented by
  1 when used with MOVSB
  2 when used with MOVSW
  4 when used with MOVSD

## Slide 11: MOVSB, MOVSW, MOVSD (2/2)
.data
src DB “Hello World!”
src_len DB $-src
dst DB src_len DUP(?)
.code
MOV CX, src_len
MOV SI, OFFSET src
MOV DI, OFFSET dst
REP MOVSB

## Slide 12: CMPSB, CMPSW, CMPSD (1/2)
Compare memory operand pointed to by SI to memory operand pointed to by DI
SI and DI are either incremented or decremented based on the value of DF
SI/DI incremented/decremented by
  1 when used with CMPSB
  2 when used with CMPSW
  4 when used with CMPSD

## Slide 13: CMPSB, CMPSW, CMPSD (2/2)
.data
src DB “Hello World!”
src_len DB $-src
dst DB “Hello! World”
.code
MOV CX, src_len
MOV SI, OFFSET src
MOV DI, OFFSET dst
REPE CMPSB

## Slide 14: SCASB, SCASW, SCASD (1/2)
Compare the value in accumulator to the memory value pointed to by DI
Useful when looking for a single value in string or array
When combined with REPNE prefix, SCASX scans until either accumulator is matched a value in memory or CX=0
When combined with REPE prefix, string is scanned while CX>0 and value in accumulator matches each subsequent value in string

## Slide 15: SCASB, SCASW, SCASD (2/2)
.data
dst DB “Hello! World”
.code
MOV CX, src_len
MOV DI, OFFSET dst
MOV AL, ‘l’
REPNE SCASB

## Slide 16: STOSB, STOSW, STOSD (1/2)
Store the contents of accumulator in the memory addressed by DI
When used with REP prefix, these instructions can be used to fill all elements of string with the same value

## Slide 17: STOSB, STOSW, STOSD (2/2)
.data
dst DB 5 DUP(?)
dst_len DW $-dst
.code
MOV CX, dst_len
MOV DI, OFFSET dst
MOV AL, ‘H’
REP STOSB

## Slide 18: LODSB, LODSW, LODSD
Load a byte/word from memory at SI into accumulator register
Used to load a single value because older value is always overwritten in accumulator