## Slide 1: Addressing Modes
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 11
  Section 11.1

## Slide 3: Addressing Modes
The set of mechanism by which an instruction can specify how to obtain its operands
An operand address provides the location where the data to be processed is stored
In an assembly instruction, the destination may be a register or memory location
Source may be an immediate value or the address of the source data

## Slide 4: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement
Stack

## Slide 5: Useful Notations
In the next slides, we use the following notations
  A denotes the contents of an address field in the instruction
  R denotes the contents of an address field in the instruction that refers to a register
  EA is the actual effective address of the location containing the referenced operand
  [X] denotes the contents of memory location X or register X

## Slide 6: Immediate Addressing (1/2)
Simplest form of addressing where operand value is present in the instruction
No memory reference other than instruction fetch is required to obtain the operand
 | Operand
Operand = A

## Slide 7: Immediate Addressing (2/2)
Example
.code
MOV AL, 10h

## Slide 8: Direct Addressing (1/3)
Direct access to the data segment is required in direct addressing mode
Address field contains the effective address of operand
Base address of segment and offset of storage location is required
EA = A

## Slide 9: Direct Addressing (2/3)
 | A
Instruction
Memory
Operand
DS
Offset

## Slide 10: Direct Addressing (3/3)
Example
.data
val DB 10h
.code
MOV al, val
MOV al, [102h] ;same as above

## Slide 11: Indirect Addressing (1/3)
Memory cell pointed to by address field contains the address of the operand
One major advantage is to reference more words if address field is less than word length
Indirect addressing can be nested or cascaded
EA = [A]
EA = [[A]]

## Slide 12: Indirect Addressing (2/3)
 | A
Instruction
Memory
Pointer to Operand
DS
Operand

## Slide 13: Indirect Addressing (3/3)
Example
.data
val DB 10h
vptr DW val
.code
MOV si, vptr
MOV al, [si]

## Slide 14: Register Addressing (1/3)
Similar to direct addressing
In this mode, a register contains the operand
Depending upon the instruction, the register may be the first operand, the second operand or both
Processing data between register does not involve memory, so it provides fastest processing of data
EA = R

## Slide 15: Register Addressing (2/3)
 | R
Instruction
Registers
Operand

## Slide 16: Register Addressing (3/3)
Example
.data
val DB 10h
.code
MOV al, ah

## Slide 17: Register Indirect Addressing (1/3)
Similar to direct addressing that offset is combined with base address of DS to get physical address
Operand is in memory cell pointed to by contents of register R
Offset lies in a pointer register (BX or BP) or index register (SI or DI)
EA = [R]

## Slide 18: Register Indirect Addressing (2/3)
 | R
Instruction
Registers
Pointer to Operand
Memory
Operand
DS
Offset

## Slide 19: Register Indirect Addressing (3/3)
Example
.data
val DB 10h
.code
MOV si, OFFSET val
MOV al, [si]

## Slide 20: Displacement Addressing (1/2)
In this addressing mode, an instruction has two address fields
Both these values are added to produce the effective address
Displacement addressing can be used as
  Relative Addressing
  Base-Register Addressing
  Indexing
EA = A + [R]

## Slide 21: Displacement Addressing (2/2)
 | R | A
Instruction
Registers
Pointer to Operand
Memory
Operand
DS
Offset

## Slide 22: Relative Addressing
Address of next instruction is added to address field to produce EA
Address of next instruction is got from PC
EA = A + [PC]

## Slide 23: Base-Register Addressing
Register contains the main memory address
Address field contains a displacement from address contained in register
Examples are Segment Registers in x86
EA = A + R

## Slide 24: Indexing
Address field contains the main memory address
Register contains the displacement from the address contained in address field
EA = A + R

## Slide 25: Stack Addressing
Operand is on the top of stack
Operand can be pushed on the stack when it is necessary to save it
Whenever operand is needed, it can be popped from the stack

## Slide 26: Extract of Addressing Modes
Mode | Algorithm | Principal Advantage | Principal Disadvantage
Immediate | Operand = A | No memory reference | Limited operand magnitude
Direct | EA = A | Simple | Limited address space
Indirect | EA = (A) | Large address space | Multiple memory reference
Register | EA = R | No memory reference | Limited address space
Register Indirect | EA = (R) | Large address space | Extra memory reference
Displacement | EA = A + (R) | Flexibility | Complexity
Stack | EA = Top of Stack | No memory reference | Limited applicability