## Slide 1: Interrupt-driven I/O and Direct Memory Access (DMA)
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 7
  Section 7.4
  Section 7.5

## Slide 3: Interrupt-driven I/O
Overcomes CPU waiting in Programmed I/O
No repeated CPU checking of devices
I/O module interrupts when ready

## Slide 4: Basic Operation from I/O Module Viewpoint
CPU issues read command
I/O module gets data from peripheral whilst CPU does other work
I/O module reads data from the peripheral
When ready, I/O module send an interrupt signal on control line to CPU and waits
CPU requests data
I/O module puts data on the data bus

## Slide 5: Basic Operation from CPU Viewpoint
Issues read command
Does some other work
Checks for interrupt at end of each instruction cycle
If interrupted by I/O module
  Save context (PC and other Registers) of current program
  Process interrupt

## Slide 6: Interrupt-driven I/O Block Diagram
Issue read command to I/O module
Read status of I/O module
Check status
Read data from I/O module
Write data into memory
Done?
CPU  I/O
I/O  CPU
Error Condition
I/O  CPU
CPU  Memory
Ready
Do something else
No
Yes
Interrupt
Next Instruction

## Slide 7: Design Issues
How to identify the module issuing the interrupt?
  Multiple Interrupt Lines between processor and I/O modules
  Software Poll to determine which module caused the interrupt
  Daisy Chain: hardware poll
  Bus Arbitration: Module gains control of the bus
How to deal with multiple interrupts?
  Each interrupt line has a priority
  Higher priority lines can interrupt lower priority lines

## Slide 8: Direct Memory Access
Drawbacks of Programmed and Interrupt-driven I/O
  Limited I/O transfer rate
  Processor tied up in managing an I/O transfer
Direct Memory Access is a better approach when transferring large amount of data
Involves additional module on system bus called DMA module
DMA module takes over control from CPU to transfer data to/from memory over system bus

## Slide 9: DMA Module Diagram
Data Count
Data Register
Address Register
Control Logic
Data Lines
Address Lines
Request to DMA
Acknowledge from DMA
Interrupt
Read
Write

## Slide 10: DMA Operation
CPU tells DMA module
  Read/Write
  Device Address
  Starting address of memory block for data
  Amount of data to be transferred
CPU carries on with other work
DMA module deals with transfer
DMA module sends interrupt to processor when finished

## Slide 11: DMA Block Diagram
Issue read block command to I/O module
Read status of I/O module
CPU  DMA
DMA  CPU
Do something else
Interrupt
Next Instruction

## Slide 12: Cycle Stealing
DMA module takes over the system bus to transfer data to and from memory
DMA must use the bus when processor does not need it
DMA can force the processor to suspend operation temporarily
  Not an interrupt so CPU does not switch context
CPU suspends just before it accesses bus
  i.e. before an operand or data fetch or a data write
Called cycle stealing because DMA module steals a clock cycle

## Slide 13: DMA Configuration
Three configuration mechanisms
  Single bus, detached DMA
  Single bus, Integrated DMA-I/O
  I/O bus

## Slide 14: Single Bus, Detached DMA
Single bus, detached DMA module
Module may support more than one devices.
Each transfer uses bus twice
  First from I/O to DMA
  Then from DMA to memory
Processor
DMA
I/O
I/O
Memory
System Bus

## Slide 15: Single Bus, Integrated DMA
Path between DMA module and I/O module
Module may support more than one devices
I/O module is not on address bus
Each transfer uses bus once
  DMA to memory
Processor
DMA
I/O
I/O
Memory
DMA
I/O
System Bus

## Slide 16: I/O Bus
Separate I/O bus
Bus supports all DMA enabled devices
Each transfer uses bus once
  From DMA to memory
Processor
DMA
I/O
I/O
Memory
I/O Bus
System Bus