## Slide 1: Integer Arithmetic
Muhammad Afzaal
m.afzaal@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 9
  Section 9.1
  Section 9.2
  Section 9.3

## Slide 3: Arithmetic and Logic Unit (ALU)
Performs the calculations
Everything else in the computer is there to serve this unit
Handles integers
May handle floating point numbers
May have a separate FPU

## Slide 4: ALU Inputs and Outputs
ALU
Control Unit
Registers
Registers
Flags

## Slide 5: Integer Representation
Positive integers are stored in computer in binary format
  e.g. 43 = 00101011
Minus sign and period cannot be stored in binary format
Signed numbers can be represented by
  Sign-Magnitude Representation
  Twos Complement Representation

## Slide 6: Sign-Magnitude Representation
MSB represents the sign of the integer
  0 for positive integers
  1 for negative integers
Remaining bits represent the magnitude of the number
1001 1101  MSB = 1 so number is negative
001 1101 = 24+23+22+20 = 16+8+4+1 = 29
Since MSB = 1, so 1001 1101 represents –29

## Slide 7: Addition and Subtraction
Normal binary addition
Monitor sign bit for overflow
For subtraction, take twos complement of the subtrahend and add to other operand
We can perform subtraction by using the addition operation

## Slide 8: Block Diagram for Adder/Subtractor
B Register
A Register
Complementer
Adder
SW
OF

## Slide 9: Multiplication
Complex operation as compared to addition/subtraction
In simple paper and pencil approach
  Work out partial product for each digit
  Take care of place of values in partial product
  Add partial products to get the final product

## Slide 10: Unsigned Binary Multiplication (1/3)
1 0 1 1
X 1 1 0 1
1 0 1 1
0 0 0 0
1 0 1 1
1 0 1 1
1 0 0 0 1 1 1 1
Multiplicand (11)
Multiplier (13)
Partial Product
Product (143)

## Slide 11: Unsigned Binary Multiplication (2/3)
n-Bit Adder
Mn-1 |  | M0
Shift and Add
Control Logic
An-1 |  | A0
Qn-1 |  | Q0
C
Multiplier
Multiplicand
Add
Shift right

## Slide 12: Unsigned Binary Multiplication (3/3)
C | A | Q | M |  | 
0 | 0000 | 1101 | 1011 | Initial Values | 
0 | 1011 | 1101 | 1011 | Add | First Cycle
0 | 0101 | 1110 | 1011 | Shift | 
0 | 0010 | 1111 | 1011 | Shift | Second Cycle
0 | 1101 | 1111 | 1011 | Add | Third Cycle
0 | 0110 | 1111 | 1011 | Shift | 
1 | 0001 | 1111 | 1011 | Add | Fourth Cycle
0 | 1000 | 1111 | 1011 | Shift | 

## Slide 13: Flowchart for Unsigned Binary Mul.
C, A  0
M  Multiplicand
Q  Multiplier
Count  n
START
Q0 = 1?
Count=0
C, A  A + M
Shift right C, A, Q
Count  Count-1
END
Yes
Yes
No
No

## Slide 14: Multiply Negative Numbers
Three possibilities to multiply negative numbers
Solution 1
  Convert to positive if required
  Multiply as previous slides like paper and pencil method
  If signs or original numbers were different, negate answer
Solution 2
  Twos complement multiplication
Solution 3
  Booth’s algorithm

## Slide 15: Two’s Complement Multiplication
In binary multiplication, multiplicand is multiplied either by 1 or 0
Multiplication of a binary number by 2n means shifting the multiplicand n bits left
Partial product is written as a 2n-bit number
Sign-bit of partial product is extended till end
Will not work if multiplier is negative

## Slide 16: Two’s Complement Multiplication
1 0 1 1
X 0 1 0 1
1 1 1 1 1 0 1 1
0 0 0 0 0 0 0 0
1 1 1 0 1 1 0 0
1 1 1 0 0 1 1 1
Multiplicand (not 11 but –5)
Multiplier (+5)
Partial Product
Product (not 55 but -25)

## Slide 17: Booth’s Algorithm (1/2)
Works with any combination of positive and negative numbers
Efficient as compared to previously discussed methods
Blocks of 1s and 0s are skipped over and just shifting is performed

## Slide 18: Booth’s Algorithm (2/2)
n-Bit Adder/Subtractor
Mn-1 |  | M0
Shift, Add and Subtract
Control Logic
An-1 |  | A0
Qn-1 |  | Q0
Q-1
Multiplier
Multiplicand
Add
Shift Arithmetic Right
Subtract

## Slide 19: Flowchart of Booth’s Algorithm
A  0, Q-1  0
M  Multiplicand
Q  Multiplier
Count  n
START
Q0 Q-1
Count=0?
A  A + M
Arithmetic Shift right A, Q, Q-1
Count  Count – 1
END
Q0=0
Q-1=1
Yes
No
A  A – M
Q0=Q-1
Q0=1
Q-1=0

## Slide 20: Booth’s Algorithm Example
A | Q | Q-1 | M |  | 
0000 | 1101 | 0 | 1011 | Initial Values | 
0101 | 1101 | 0 | 1011 | A = A–M | First Cycle
0010 | 1110 | 1 | 1011 | SAR | 
1101 | 1110 | 1 | 1011 | A = A+M | Second Cycle
1110 | 1111 | 0 | 1011 | SAR | 
0011 | 1111 | 0 | 1011 | A = A–M | Third Cycle
0001 | 1111 | 1 | 1011 | SAR | 
0001 | 1111 | 1 | 1011 | Do Nothing | Fourth Cycle
0000 | 1111 | 1 | 1011 | SAR |